## Slide 1: 128K x 8 CMOS Static RAM
Karthik M. B (2016EEY7523)
Souradeep Naskar (2016EEN2515)
Avinash Kumar (2016EEN2542)
Sumit Diware (2016JVL2111)
Sharath B. K (2016JVL2109)
Under the guidance of Dr. Kaushik Saha

## Slide 2: Targeted Specifications
128K × 8 bit CMOS Static RAM [Cypress Semiconductors- CY7C1019CV33 ]
Key Features : Automatic power-down when deselected
Address width : 17 bit ()
Data width : 8 bit ()
Operating Voltage : 1V ± 10%
Operating Temperature : Commercial (0 ~ 70°C)
Technology Node : UMC 90nm
Cycle time : 15 ns (min)
Address to Data Valid time : 15ns (max)

## Slide 3
Gantt Chart

## Slide 4: Array Partitioning
We have 17 address lines => 217 Memory locations of 8 bit each
i.e. 220 bits.
To get a square array we choose 210 bit lines and 210 word line.
Since our package pin configuration is symmetric , to facilitate routing we chose quadrant alignment of the cores.
i.e. 4 banks of 32k x 8bits

## Slide 5
However for improving speed we prefer smaller bank size to have smaller word line and bit line capacitances.
Therefore we opt for 8 banks of 16k x 8bits each .
But the decoder logic complexity increases exponentially as the number of banks increases and hence we don’t choose banks of smaller size.

## Slide 6: Metal Planning
Layers | Application | Resistance( Ω/μm) | Capacitance( aF/μm)
Metal Layer 1 | Local Routing | 0.865 | 88.09
Metal Layer 2 | Word Line Strapping | 0.727 | 70.96
Metal Layer 3 | Bit Line | 0.727 | 62.43
Metal Layer 4 | Bit Line Complement | 0.727 | 57.83
Metal Layer 5 | Address Routing | 0.727 | 54.99
Metal Layer 6 | Control Routing | 0.727 | 54.78
Metal Layer 7 | VSS | 0.159 | 71.11
Metal Layer 8 | VDD | 0.161 | 67.57

## Slide 7: Address Lines Division
No. of Row Decoding Bits = 5 (A0 – A4)
No. of Column Decoding Bits = 9 (A5 – A13)
No. of Bits for bank Selection = 3 (A14 – A16)

## Slide 8: Floor Planning and Routing

## Slide 9
I
/O
BUFFERS
I
/O
BUFFERS
A0
A1
A2
A3
I/O0
I/O1
VCC
VSS
I/O2
I/O3
A4
A5
A6
A7
A16
A15
A14
A13
I/O7
I/O6
VSS
VCC
I/O5
I/O4
A11
A10
A9
A8
A12
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ADDRESS TRANSITION DETECTOR
BLOCK DECODER
TIMING AND CONTROL CIRCUIT
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER

## Slide 10
I
/O
BUFFERS
I
/O
BUFFERS
A0
A1
A2
A3
I/O0
I/O1
VCC
VSS
I/O2
I/O3
A4
A5
A6
A7
A16
A15
A14
A13
I/O7
I/O6
VSS
VCC
I/O5
I/O4
A11
A10
A9
A8
A12
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ADDRESS TRANSITION DETECTOR
BLOCK DECODER
TIMING AND CONTROL CIRCUIT
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER

## Slide 11
I
/O
BUFFERS
I
/O
BUFFERS
A0
A1
A2
A3
I/O0
I/O1
VCC
VSS
I/O2
I/O3
A4
A5
A6
A7
A16
A15
A14
A13
I/O7
I/O6
VSS
VCC
I/O5
I/O4
A11
A10
A9
A8
A12
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
16K × 8 bit
SRAM Core
PRECHARGE
SENSE AMPLIFIER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ROW DECODER
ROW DECODER
WRITE BUFFER
ADDRESS TRANSITION DETECTOR
BLOCK DECODER
TIMING AND CONTROL CIRCUIT
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER
COLUMN DECODER

## Slide 12: Comparison of various SRAM Cell Architectures
Ref : Binh-Son LE, Thanh-Tri VO, “SRAM Cell for High Noise Margin & Soft Errors Tolerance in Nanoscale Technology”, IEEE 2014
Parameters | 6T SRAM | 7T SRAM | 8T SRAM | 9T SRAM | 10T SRAM
Read Margin (mV) | 156 | 156 | 330 | 330 | 176
Write Margin (mV) | 551 | 796 | 598 | 598 | 423
Size | X | 1.48X | 1.24X | 1.95X | 2.78X
Read Delay (psec) | 555 | 842 | 731 | 755 | 555
Write Delay (psec) | 50.6 | 39.1 | 38.3 | 41.4 | 79.3
Leakage Power (nW) | 242 | 250 | 322 | 331 | 488

## Slide 13: Advantages of 6T Cell
Lower power dissipation - 6T SRAM cell has less leakage current because less number of transistors are being used compared to 7T, 8T, 9T SRAM cell architecture.
Good stability - 6T SRAM cell has good stability as compared to 4T SRAM cell.
As 4T SRAM cell has lower value of SNM (Static Noise Margin), high standby
current and is not as fast as the 6T cell.
Symmetric structure - Helps during fabrication of device.

## Slide 14
6T SRAM Cell
M1 M3 : Pull down transistors.
M2 M4 : Pull up transistors.
M5 M6 : Access transistors
Basic SRAM cell
For Read Stability : M1,M3 pull down transistors should be stronger than the M5,M6 access transistors
For Write Stability : M2,M4 pull up transistors should be weaker than the M5,M6 access transistors
M6

## Slide 15
Cell Ratio and Pull-up Ratio
Cell Ratio : It is the ratio between size of the pull down transistor to that of access transistor during the read operation.
Pull up Ratio : It is the ratio between size of the pull up transistor to that of access transistor during the write operation.

## Slide 16
WL
BL
V
DD
M
5
M
6
M
4
M
1
V
DD
V
DD
V
DD
BL
Q
=
1
Q
=
0
C
bit
C
bit
CMOS SRAM Analysis (Read)

## Slide 17
Cell Ratio
Voltage Rise (V)
CMOS SRAM Analysis (Read)
CR(min)
1.1

## Slide 18
BL
=
1
BL
=
0
Q
=
0
Q
=
1
M
1
M
4
M
5
M
6
V
DD
V
DD
WL
CMOS SRAM Analysis (Write)

## Slide 19
Pull Up Ratio
Cell Voltage (V)
CMOS SRAM Analysis (Write)
PR(max)
1.25

## Slide 20
Static Noise Margins
The static noise margin (SNM) measures how much noise can be applied to the inputs of the two cross-coupled inverters before a stable state is lost (during hold or read) or a second stable state is created (during write).
Acceptable value of SNM are used to decide the optimum values of CR, PR.
Cadence Virtuoso was used for circuit simulation and the corresponding Butterfly curves were plotted using MATLAB.
Ref : 1. EVERT SEEVINCK, FRANS J. LIST, AND JAN LOHSTROH, M “Static-Noise Margin Analysis of MOS SRAM Cells”, IEEE 1987
2. CMOS VLSI Design: A Circuits and Textbook by David Harris and Neil Weste

## Slide 21
Read Static Noise Margins
CR | SNM (V)
2 | 0.141
2.5 | 0.155
3 | 0.169
3.5 | 0.184
4 | 0.198

## Slide 22
Write Static Noise Margins
PR | SNM (V)
1 | 0.523

## Slide 23
Hold Static Noise Margins
CR | SNM (V)
2 | 0.318

## Slide 24
Read Static Noise Margins around Process Corners
Corner | SNM (V)
SS | 0.163

## Slide 25
Write Static Noise Margins around Process Corners
Corner | SNM (V)
SS | 0.509

## Slide 26
Hold Static Noise Margins around Process Corners
Corner | SNM (V)
SS | 0.3536

## Slide 27
Bitline Twisting
Bit line twisting will make sure that effect of coupling noise will be symmetric on both BL and BL_BAR, and thus effect of coupling noise will be reduced.
Bit line twisting scheme, where bit line is twisted after every 16 columns (or after every 16th Word Line).
There are total 512 columns. Bit line is twisted 32 times in each core.

## Slide 28
SRAM Cell Sizing:
The access transistors were chosen to be of minimum size so as to minimize the bitline capacitance.
Considering acceptable noise margins pull-up ratio was chosen to be 1 and cell ratio was 2.
Optimum CR = 2 & PR = 1.0
Sizing of Transistors : L= 80 nm
Pull-up Transistors : W = 120 nm
Access Transistors : W = 120 nm
Drive Transistors : W = 240 nm
Process Corner : Slow NMOS Slow PMOS (ss)

## Slide 29
Pre-charge Scheme
Pre-charging of bitlines is done before reading a cell.
When read operation is initiated, after the block level decoding, the pre-charge enable signal of the particular block is asserted.
After pre-charging the pre-charge signal is de-asserted then the particular is asserted and sense amplifiers of the block are enabled.

## Slide 30
Pre-charge Circuit
M1, M2 : Pre-Charge Transistors.
M3 : Equalization Transistor.
Pre_En : Pre-charge enable signal.
, : Bitline and its compliment.

## Slide 31
Calculations of bitline transients
Capacitance Calculations
  For BL we planned to use Metal 3.
  Metal 3 Parasitic extractions
    R = 0.727 Ω/μm , C = 62.43 aF/ μm.
  =
  +
Resistance Calculations
  .
  = 744.448

## Slide 32
Bitline pre-charge settling analysis
Circuit Setup:
  We have chosen
  .
  (Used for both and .)
  Over estimated the calculations a little to include the other parasitic effects.
  (like parasitics of the sense amplifier and coupling capacitances.)

## Slide 33
Pre-charge Settling Time Analysis

## Slide 34
Width of Pre-charge Transistors(nm) | 90% Settling Time(ns)
120 | 7.49
220 | 5.21
320 | 3.95
420 | 3.20
520 | 2.75
620 | 2.66
720 | 2.57

## Slide 35: Address Lines Division
No. of Row Decoding Bits = 5 (A0 – A4)
No. of Column Decoding Bits = 9 (A5 – A13)
No. of Bits for bank Selection = 3 (A14 – A16)

## Slide 36
Decoder Design Strategy
We have divided the decoding into two stages.
  Pre-decoding. (To be done near the address pins of the chip)
  Post-decoding. (To be done near the memory core)
Ex. BL0 = =
NOR operation is the pre-decoding stage, AND operation is the Post-decoding stage.

## Slide 37
Row Decoder circuit
Pre-Decoding
Post-Decoding

## Slide 38
Another Decoder strategy
To reduce the decoder delay we distributed the pre-decoding part in multiple stages.
It reduces the delay and transistor count.

## Slide 39
Pre Decoder
stage
Post Decoder
Stage
Ref: Arvind Kumar Mishra, Debiprasad Priyabrata Acharya, Pradeep Kumar Patra “Novel Design Technique of Address Decoder for SRAM”
IEEE 2014 International Conference on Advanced Communication Control and Computing Technologies(ICACCCT)
Decoder 5 X 32

## Slide 40
Decoder Types | Critical Path Delay (psec)
Row Decoder | 123
Column Decoder | 415
Row Decoder (Novel Technique) | 79
Column Decoder (Novel Technique) | 227
Decoders Comparison

## Slide 41
Sense Amplifier Design
Since our main goal is the to achieve low access time, sense amplifier should be fast.
For our access time requirement we found that full analog circuit is slow.
We implemented the sense amplifier with analog and digital mixed stage.
With which we are able to detect a 6mV difference on the bit-lines with almost an edge triggered response.

## Slide 42
Sense Amplifier Design (cont.)
A Double-Tail Latch-Type Voltage Sense Amplifier[*]
[*] Daniel Schinkel, Eisse Mensink, Eric Klumperink, Ed van Tuijl, Bram Nauta “A Double-Tail Latch-Type Voltage Sense Amplifier with 18ps Setup + Hold Time” . 2007 IEEE International Solid-State Circuits Conference.

## Slide 43
Sense Amplifier Simulation
Vp
Vn

## Slide 44
Estimation of read pulse width(Word Line pulse width)
Read Enable pulse width proportional
).
Here we took , the time taken to create enough difference(6mV) on bit-lines to have valid sense amplifier output.
Pulse width is approximately 102psec.

## Slide 45
Single Memory Cell Simulation

## Slide 46
Optimized 6T Cell Layout
Parameter | Value
Length | 2.105 um
Width | 1.74 um
Area | 3.67 sq.um

## Slide 47
Optimized 4x4 Memory Block
Parameter | Value
Length | 7.77 um
Width | 5.54 um
Area | 43.04 sq.um
Area / cell | 2.69 sq.um

## Slide 48
Bitline Twisting
Metal Layer 4 is used for twisting one of the bit lines.

## Slide 49
Word Line Driver
We select the
Overall effective fan-out,
Normalized propagation delay (tp/(tpopt)) as a function of f

## Slide 50
Word Line Driver
where N  number of stages
Solving
We choose

## Slide 51
Address Transition Detector

## Slide 54
ATD Simulation

## Slide 55
Modified Edge Detector

## Slide 56
Modified Monostable Multivibrator
Corner | Pulse Width (ps)
ss | 581
tt | 531
ff | 543

## Slide 57
ATD Multi-Trigger Simulation

## Slide 58
Memory Bank (256x512)

## Slide 59
Memory Bank
Parameters | Values
Length | 1066 um
Width | 368 um
Area/Cell | 3 sq.um/Cell

## Slide 60
Sense Amplifier Layout

## Slide 61
Post PEX simulation of Sense Amplifier

## Slide 62
Post PEX analysis of Sense Amplifier
Parameter | Value
Sensitivity | 228 mV
Delay | 261 ps
Area | 8.06 µm2 (Width = 1.47 µm )
Power (Per one SEN_EN) | 31.2 µW

## Slide 63
Pre-charge Circuit Layout
Parameter | Value
Length | 0.84 µm
Width | 1.38 µm
Area | 1.15 µm2

## Slide 64
Word-Line Driver Layout
Parameter | Value
Length | 1.725 µm
Width | 38.86 µm
Area | 67.03 µm2

## Slide 65
Word-Line Driver Layout (Enlarged)

## Slide 66
Post PEX simulation of Word Line Driver
Parameter | Value
Delay (90% of VDD) | 183.57 ps

## Slide 67
Write Buffer Schematic

## Slide 68
Row Pre-Decoder Layout

## Slide 69
Column Pre-Decoder Layout

## Slide 70
Column Decoder(Final Stage) Layout

## Slide 71
Block Decoder Layout

## Slide 72
Decoder Dimensions
Instance | Area ( µm2 )
Row Pre-Decoder | 220.56
Column Pre-Decoder | 126.46
Column Final-Stage | 293.03
Block Decoder | 39.21

## Slide 73
ATD – Edge Detector

## Slide 74
ATD – Wired OR

## Slide 75
ATD – Monostable Multivibrator

## Slide 76
Integrated Memory Bank
(512 256 bits)
Parameter | Value
Width | 408.185 µm
Length | 1075.925 µm
Area (per bank) | 0.439 mm2

## Slide 77
Sense Amplifier – Core Interface

## Slide 78
Pre Charge – Core Interface

## Slide 79
Word-Line Driver – Core Interface