## Slide 1: Memory Design and Testing – EE787
Kaushik Saha
Contact: ksaha_2000@yahoo.com, mobile-98110-64398

## Slide 2: Course Logistics (TBD)
Class Representative
Class Newsgroup manager –
I need a class list (Soft copy)
Grading Policy
  Project
    Project Review - 60
      Every class will project review
      every project group will present its progress every alternate weel
    Project Document - 20
  Majors - 20

## Slide 3: Texts
Semiconductor Memories, A Handbook of Design, Manufacture and Application (2nd Ed) – Betty Prince
  John Wiley & Sons UK, ISBN 0 471 92465 2; 0 471 94294 2 (pbk)
Journal articles and Web material
Course material will be made available on
  USB drive
  Course newsgroup

## Slide 4: Agenda of Topics
1 Memory hierarchy in digital systems
2) Static RAM
a. Types
b. Overall architecture
c. SRAM Cell
i. Design
ii. Layout
iii. Noise issues and margins
iv. Assembly of core
d. Peripheral circuitry
i. Decoding
ii. Array conditioning for r/w
iii. Sensing
iv. Writing
v. Synchronisation
3) Dynamic RAM
a. Types
b. Cell design
c. Assembly of core
i. Core architectures
d. Peripheral circuitry
i. Sensing
ii. Elevated voltage supplies
e. Modern high speed DRAM
i. EDO,
ii. SDR,
iii. DDR)

## Slide 5: Agenda of Topics cont’d
4) Non volatile memories
a. ROM
i. Array design
b. EPROM
i. Cell and array design
c. EEPROM
i. Tunneling phenomena
ii. EEPROM cell
1. Hot carrier based operation
2. Tunneling based operation
d. Flash memories
i. Cell operation and design
ii. Types of modern high density flash memories
1. NOR flash
2. NAND flash

## Slide 6: Classification of Memories
RW | Memory | NVRWM | ROM
Random Access | Non-Random Access | EPROM EEPROM | Mask Programmed
SRAM (Static) DRAM (Dynamic) | FIFO (Queue) LIFO (Stack) SR (Shift Register) CAM (Content Addressable) | FLASH | PROM (Fuse Programmed)

## Slide 7: Feature Comparison Between Memory Types

## Slide 8: Memory selection : cost and performance
DRAM, EPROM
  Merit : cheap, high density
  Demerit : low speed, high power
SRAM
  Merit : high speed or low power
  Demerit : expensive, low density
Large memory with cost pressure :
  DRAM
Large memory with very fast speed :
  SRAM or
  DRAM main + SRAM cache
Back-up main for no data loss when power failure
  SRAM with battery back-up
  EEPROM

## Slide 9: The Need for Innovation in Memory Industry
The learning rate (viz. the constant b) is the highest for the memory industry
  Because prices drop most steeply among all ICs
    Due to the nature of demand + supply
  Yet margins must the maintained
Techniques must be applied to reduce production cost
Often, memories are the launch vehicles for a technology node
  Leads to volatile nature of prices

## Slide 10: Memory Hierarchy of a Modern Computer System
By taking advantage of the principle of locality:
  Present the user with as much memory as is available in the cheapest technology.
  Provide access at the speed offered by the fastest technology.
Control
Datapath
Secondary
Storage
(Disk)
Processor
Registers
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
On-Chip
Cache
1s
10,000,000s
(10s ms)
Speed (ns):
10s
100s
100s
Gs
Size (bytes):
Ks
Ms
Tertiary
Storage
(Tape)
10,000,000,000s
(10s sec)
Ts
Notes: The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in details in the next lecture on caches).
+1 = 16 min. (X:56)

## Slide 11: How is the hierarchy managed?
Registers <-> Memory
  by compiler (programmer?)
cache <-> memory
  by the hardware
memory <-> disks
  by the hardware and operating system (virtual memory)
  by the programmer (files)

## Slide 12: Memory Hierarchy Technology
Random Access:
  “Random” is good: access time is the same for all locations
  DRAM: Dynamic Random Access Memory
    High density, High power, cheap, slow
    Dynamic: need to be “refreshed” regularly
  SRAM: Static Random Access Memory
    Low density, Lower power, expensive, fast
    Static: content will last “forever”(until lose power)
“Not-so-random” Access Technology:
  Access time varies from location to location and from time to time
  Examples: Disk, CDROM
Notes: The technology we used to build our memory hierarchy can be divided into two categories: Random Access and Non-so-Random Access.
Unlike all other aspects of life where the word random usually associates with bad things, random, when associates with memory access, for the lack of a better word, is good!
Because random access means you can access any random location at any time and the access time will be the same as any other random locations.
Which is NOT the case for disks or tape where the access time for a given location at any time can be quite different from some other random locations at some other random time.
As far as Random Access technology is concerned, we will concentrate on two specific technologies: Dynamic RAM and Static RAM.
The advantages of Dynamic RAMs are high density, low cost, and low power so we can have a lot of them without burning a hole in our budget or our desktop.
The disadvantages of DRAM are they are slow. Also they will forget what you tell them if you don’t remind them constantly (Refresh). We will talk more about refresh later today.
SRAM only has one redeeming feature: it is fast. Other than that, they have low density, expensive, and burn a lot of power. Oh, SRAM actually has another redeeming feature. They will not forget what you tell them. They will keep whatever you write to them forever.
Well “forever” is a long time. So lets just say it will keep your data as long as you don’t pull the plug on your computer.
In the next two lectures, we will be focusing on DRAMs and SRAMs.
We will not get into disk until the Virtual Memory lecture a week from now.
+3 = 19 min. (X:59)

## Slide 13: Main Memory Background
Performance of Main Memory:
  Latency: Cache Miss Penalty
    Access Time: time between request and word arrives
    Cycle Time: time between requests
  Bandwidth: I/O & Large Block Miss Penalty (L2)
Main Memory is DRAM : Dynamic Random Access Memory
  Dynamic since needs to be refreshed periodically Addresses divided into 2 halves (Memory as a 2D matrix):
    RAS or Row Access Strobe
    CAS or Column Access Strobe
Cache uses SRAM : Static Random Access Memory
  No refresh (6 transistors/bit vs. 1 transistor) Size: DRAM/SRAM ­ 4-8 Cost/Cycle time: SRAM/DRAM ­ 8-16

## Slide 14: Memory Interfaces
Address i/ps
  Maybe latched with strobe signals
Write Enable (/WE)
  To choose between read / write
  To control writing of new data to memory
Chip Select (/CS)
  To choose between memory chips / banks on system
Output Enable (/OE)
  To control o/p buffer in read circuitry
Data i/os
  For large memories data i/p and o/p muxed on same pins,
    selected with /WE
Refresh signals

## Slide 15
N words
M bits per word
N select lines
1:N decoder
very inefficient design
difficult to place and route
Word N-1
Word N-2
Word 2
Word 1
Word 0
S0
S1
S2
SN-2
SN-1
Single
Storage
Cell
M bit output word
Memory - Basic Organization

## Slide 16: Memory - Real Organization
S0
SR-1
Row
Decoder
Log2R
Address
Lines
- - - - CxM bits - - - -
C of M bit words row 0
C of M bit words row 1
C of M bit words row 2
C of M bit words row R-2
C of M bit words row R-1
Array of R x C words
------------- columns ------------ CxM
------------- rows R------------
Log2C
Address
Lines
Column Select
M bit data word
N = R * C

## Slide 17: Memory - Organization and Cell Design Issues
aspect ratio (height : width) should be relative square
  Row / Column organisation (matrix)
  A_R = log2(R); A_C = log2(C)
  A_R + A_C = N_address_bits
  N = 2N_address_bits = R*C
number of rows should be power of 2
  number of bits in a row
sense amplifiers to amplify the voltage from each memory cell
R -> 2A_R row decoder
C -> 2A_C column decoder
  implement M of the column decoders (M bits, one per bit)
    M = output word width

## Slide 18: Array-Structured Memory Architecture L address bits – K bit row address, L-K bit column address

## Slide 19: Hierarchical Memory Architecture

## Slide 20: SRAM Application Areas
Main memory in high performance small system
Main memory in low power consumption system
Simpler and less expensive system if without a cache
Battery back-up
Battery operated system

## Slide 21: SRAM Performance vs Application Families

## Slide 22: Typical Application Scenarios
Hand phone and Cache
MMU
FPU
BIU
ALU
CORE
L1
16KB
L2
256KB
64MB
I/O
PCI
ISA
SRAM
DRAM
i586 based PC

## Slide 23: Overview of SRAM Types

## Slide 24: Logic Diagram of a Typical SRAM (Asynch)
Write Enable is usually active low (WE_L)
Din and Dout are combined to save pins:
  A new control signal, output enable (OE_L) is needed
  WE_L = 0, OE_L = 1
    D serves as the data input pin
  WE_L = 1, OE_L = 0
    D is the data output pin
  Both WE_L = 1, OE_L = 1
    Result is unknown. Don’t do that!!!
A0-AN
D
OE_L
2
N
words
x M bit
SRAM
M
WE_L
CS!
Notes: Here is the logic diagram of a typical SRAM. In order to save pins, Din and Dout are combined into a set of bidirectional pins so you need a new control signal: Output Enable.
Both write enable and output enable are usually asserted low.
When Write Enable is asserted, the D pins serve as the data input pin.
When Output Enable is asserted, the D pins serve as the data output pin.
+1 = 33 min. (Y:13)

## Slide 25: SRAM Architecture

## Slide 26: Basic Memory Read Cycle
System selects memory with /CS=L
System presents correct address (A0-AN)
System turns o/p buffers on with /OE=L
System tri-states previous data sources within a permissible time limit (tOLZ or tCLZ)
System must wait minimum time of tAA, tAC or tOE to get correct data

## Slide 27: Basic Memory Write Cycle
System presents correct address (A0-AN)
System selects memory with /CS=L
System waits a minimum time equal to internal setup time of new addresses (tAS)
System enables writing with /WE=L
System waits for minimum time to disable o/p driver (twz)
System inputs data and waits minimum time (tDW) for data to be written in core, then turns off write (/WE=H)

## Slide 28: Memory Timing: Definitions

## Slide 29: Memory Timing: Approaches

## Slide 30: The system level view of Async SRAMs

## Slide 31: The system level view of synch SRAMs

## Slide 32: Typical Async SRAM Timing
Write Timing:
D
Read Timing:
WE_L
A
Write
Hold Time
Write Setup Time
A
D
OE_L
2
N
words
x M bit
SRAM
N
M
WE_L
Data In
Write Address
OE_L
High Z
Read Address
Junk
Read Access
Time
Data Out
Read Access
Time
Data Out
Read Address
Notes: For write, you set up your address and data on the A and D pins and then you generate a write pulse that is long enough for the write access time.
For simplicity, I have assumed the Write setup time for address and data to be the same. In real life, they can be different.
For read operation, you have disasserted Wr Enable and assert Output Enable. Since you are supplying garbage address here so as soon as you assert OE_L, you will get garbage out.
If you then present an valid address to the SRAM, valid data will be available at the output after a delay of the Write Access Time.
SRAM’s timing is much simpler than the DRAM timing which I will show you later.
+1 = 34 min. (Y:14)

## Slide 33: SRAM Read Timing (typical)
tAA (access time for address): how long it takes to get stable output after a change in address.
tACS (access time for chip select): how long it takes to get stable output after CS is asserted.
tOE (output enable time): how long it takes for the three-state output buffers to leave the high- impedance state when OE and CS are both asserted.
tOZ (output-disable time): how long it takes for the three-state output buffers to enter high- impedance state after OE or CS are negated.
tOH (output-hold time): how long the output data remains valid after a change to the address inputs.

## Slide 34: SRAM Read Timing (typical)
stable
stable
stable
valid
valid
valid
tAA
tOZ
 tAA
tOE
tACS
tOZ
tOE
Max(tAA, tACS)
tOH
ADDR
CS_L
OE_L
DOUT
WE_L = HIGH

## Slide 35: SRAM Architecture and Read Timings
tAA
tACS
tOE
tOZ
tOH

## Slide 36: SRAM write cycle timing
/WE controlled
/CS controlled

## Slide 37: SRAM Architecture and Write Timings
Write driver
tWP-tDW
Setup time = tDW
tDH

## Slide 38
Array Organization
  common bit precharge lines
  need sense amplifier
SL0
SL1
SL2
SRAM Array

## Slide 39: SRAM Architecture

## Slide 40: SRAM Architecture

## Slide 41: Simple 4x4 SRAM Memory
A0
Row Decoder
BL
WL[0]
A1
A2
Column Decoder
sense amplifiers
write circuitry
!BL
WL[1]
WL[2]
WL[3]
bit line precharge
2 bit width
M=2
A_R = 2
R = 2A_R = 4
A_C = 1
C = 2A_C x M = 4
N_ADDR = A_R + A_C = 3
Array size =
R x C = 16
clocking and control ->
enable
read precharge
A0!
WE! , OE!
Notes: To decrease the bit line delay for reads – use low swing bit lines, i.e., bit lines don’t swing rail-to-rail, but precharge to Vdd (as 1) and discharge to Vdd – 10%Vdd (as 0). (So for 2.5V Vdd, 0 is 2.25V.) Requires sense amplifiers to restore to full swing.
Write circuitry – receives full swing from sense amps – or writes full swing to the bit lines

## Slide 42: Simple 4x4 SRAM Memory
A0
Row Decoder
BL
WL[0]
A1
A2
Column Decoder
sense amplifiers
write circuitry
!BL
WL[1]
WL[2]
WL[3]
bit line precharge
2 bit width
M=2
A_R = 2
R = 2A_R = 4
A_C = 1
C = 2A_C x M = 4
N_ADDR = A_R + A_C = 3
Array size =
R x C = 16
clocking and control ->
enable
read precharge
A0!
WE! , OE!
Notes: To decrease the bit line delay for reads – use low swing bit lines, i.e., bit lines don’t swing rail-to-rail, but precharge to Vdd (as 1) and discharge to Vdd – 10%Vdd (as 0). (So for 2.5V Vdd, 0 is 2.25V.) Requires sense amplifiers to restore to full swing.
Write circuitry – receives full swing from sense amps – or writes full swing to the bit lines

## Slide 43: SRAM Cell Design
Memory array typically needs to store lots of bits
  Need to optimize cell design for area and performance
  Peripheral circuits can be complex
    Smaller compared to the array (60-70% area in array, 30-40% in periphery)
Memory cell design
  6T cell full CMOS
  4T cell with high resistance poly load
  TFT load cell

## Slide 44: Anatomy of the SRAM Cell
Write:
set bit lines to new data value
  b’ = opposite of b
raise word line to “high”
  sets cell to new state
    May need to flip old state
Read:
set bit lines high
set word line high
see which bit line goes low
->

## Slide 45: SRAM Cell Operating Principle
Inverter Amplifies
  Negative gain
  Slope < –1 in middle
  Saturates at ends
Inverter Pair Amplifies
  Positive gain
  Slope > 1 in middle
  Saturates at ends

## Slide 46: Bistable Element
Stability
§ Require Vin = V2
§ Stable at endpoints
recover from pertubation
§ Metastable in middle
Fall out when perturbed
Ball on Ramp Analogy

## Slide 47: SRAM Cell technologies
Bipolar ECL : NPN with dual emitter
NMOS load
A) Enhancement : additional load gate bias
B) Depletion : no additional load gate bias
High Load
Resistance (4T)
Full CMOS
(6T)
Thin Film
Transistors

## Slide 48: 6T & 4T cell Implementation
6T Bistable Latch
4T Bistable Latch
High resistance poly

## Slide 49: Reading a Cell
Icell
DV = Icell * t
-----
Cb
Sense Amplifier

## Slide 50: Writing a Cell
1 -> 0
0 -> 1

## Slide 51: SRAM Cell Analysis (Read)
!BL=1
BL=1
WL=1
M1
M4
M5
M6
Q=1
!Q=0
Cbit
Cbit
Cell Ratio (CR) = (WM1/LM1)/(WM5/LM5)
V!Q = [(Vdd - VTn)(1 + CR (CR(1 + CR))]/(1 + CR)
Notes: M5 in saturation, M1 in linear mode

## Slide 52: Read Voltages Ratios
Vdd = 2.5V
VTn = 0.5V
Notes: To avoid read-disturb, the voltage on node !Q should remain below the trip point of the inverter pair for all process, noise, and operating conditions. CRs of no less than 1.2 (most microprocessor fabs use a minimum cell ratio of 1.25 to 2)
Simulations should be done at high Vdd and low VTn (and considering process variations and misalignments)

## Slide 53: SRAM Cell Analysis (Write)
!BL=1
BL=0
WL=1
M1
M4
M5
M6
Q=1
!Q=0
Pullup Ratio (PR) = (WM4/LM4)/(WM6/LM6)
VQ = (Vdd - VTn) ((Vdd – VTn)2 – (p/n)(PR)((Vdd – VTn - VTp)2)
Notes: State shown is that before write takes effect (1 is stored, trying to write a 0)
In order to write the cell, the pass gate M6 must be more conductive than the M4 to allow node Q to be pulled to a value low enough for the inverter pair (M2/M1) to begin amplifying the new data.
The maximum ratio of the pullup size to that of the pass gate required to guarantee that the cell is writable – M6 in linear, M4 in saturation

## Slide 54: Write Voltages Ratios
Vdd = 2.5V
|VTp| = 0.5V
p/n = 0.5
Notes: In order to write the cell, node Q must be pulled to a value low enough to trip the inverter combination – so pulling Q below VTn (0.5V) is required.
The limiting case for the write operation occurs at high Vdd when the pfet is strong (mup high, VTp low) and the nfet is weak (mun low, VTn high)
Typicaly, the widths of the pullup devices are sized at or near process minimum. Longer than minimum channel lengths may also be emplyed to further reduce the pullup ratio. This is necessary since the read sizing of the SRAM cell dictates that the pass gate sizing should be minimized to prevent read disturbs.

## Slide 56: Cell Sizing
Keeping cell size minimized
Minimum sized pull down fets
  Requires minimum width pull downs
  longer than minimum length access transistors for CR
  But upsizing access transistors increases capacitive load on the word lines
  limits the current discharged on the bit lines
  lowers speed of the read cycle
Minimum sized access transistors
  Need to boost the width of the pull downs
  Reduces the loading on the word lines
  increases the storage capacitance in the cell
  both are good! – but cell size may be slightly larger

## Slide 57: Cell Static Noise Margin
Cell state may be disturbed by
DC
  Layout pattern offset
  Process mismatches
    non-uniformity of implantation
    gate pattern size errors
AC
  Alpha particles
  Crosstalk
  Voltage supply ripple
  Thermal noise
SNM = Maximum Value of Vn
Without flipping cell state

## Slide 58: SNM: Butterfly Curves
1
1
2
2
2
2
1
1
SNM
SNM

## Slide 59: Static noise margin (SNM) of the unstressed SRAM cell.
The window in the ``butterfly'' curve
illustrates the hardiness against noise.
Figure of merit for an SRAM cell is its static noise margin (SNM).
It can be extracted by nesting the largest possible square in the two voltage transfer curves (VTC) of the involved CMOS inverters
The SNM is defined as the diagonal length of the square, given in volts.
When an external DC noise is larger than the SNM, the state of the SRAM cell can change and data is lost.

## Slide 60: Static Noise Margin
SNM quantifies the amount of voltage noise required at the internal nodes of a bitcell to flip the cell’s contents.
Degraded SNM can limit voltage scaling for SRAM designs.
Inverter 2
Inverter 1
SNM is length of diagonal of the largest embedded square on the butterfly curve
WL
BLB
BL
Q
QB
M1
M2
M3
M4
M5
M6
VN
VN
[1]

## Slide 61: Cont’d
Moves upward
Moves to the left
SNM is lower during read access because the VTC is degraded by the voltage divider across the access transistor (M2,M5) and drive transistor (M1,M4)[2]
SNM Butterfly Curve
The minimum supply voltage of SRAMs is determined by both Read SNM and Write SNM levels; reducing Vth in the NMOS transistor improves Write SNM but worsens Read SNM.

## Slide 62: SNM during HOLD and READ
Read SNM is worst-case
WL=0
BLB
BL
1
0
M1
M2
M3
M4
M5
M6
WL=1
BLB prech 1
BL prech 1
1
0
M1
M2
M3
M4
M5
M6
[1]

## Slide 63: SNM Derivation 6T Cell
Sat
Sat
Lin
Lin
IQ1=IQ5
IQ2=IQ4

## Slide 64: SNM Derivation 6T Cell (cont’d)
First order device model
Current Eqns
Loop Voltage Eqns
where

## Slide 65: SNM Derivation 6T Cell (cont’d)
Substituting & Simplifying
where
where
Linearized
characteristics

## Slide 66: SNM Derivation 6T Cell (cont’d)
Eliminate VDS2
where
Use identical root condn

## Slide 67: References
Static-noise margin analysis of MOS SRAM cells E Seevinck, FJ List, J Lohstroh - Solid-State Circuits, IEEE Journal of, 1987 - ieeexplore.ieee.org
Analyzing Static Noise Margin for Sub-threshold SRAM in 65nm CMOS BH Calhoun, A Chandrakasan - www-mtl.mit.edu
The impact of intrinsic device fluctuations on CMOS SRAM cell stability AJ Bhavnagarwala, X Tang, JD Meindl - IEEE Journal of Solid-State Circuits, 2001 – ieeexplore.ieee.org
J. Lohstroh, E, Seevinck,, and J, de Groot, “Worst-case static noise margin criteria for logic clrcuils and their mathematical equivalence,” IEEE J. Solid-State Circuits, vol. SC-18, no. 6, pp. 803–807, Dec.1983,

## Slide 68
VDD
GND
SEL
B-
Q/
B+
Q
SEL MOSFET
PMOS
Pull Up
NMOS
Pull Down
Substrate
Connection
N Well
Connection
6T Cell Layout

## Slide 69
6T SRAM Array Layout

## Slide 70: Another 6T Cell Layout Stick Diagram
bit
bit’
These four contacts shared with (mirrored) cell below
word
Gnd
GND and contact shared with cell to left
VDD
T
T
T
T
T
T
2 Metal Layer Process

## Slide 71: 6T Array Layout (2x2) Stick Diagram
bit
bit’
word
Gnd
VDD
word
VDD
Gnd
bit
bit’
VDD

## Slide 72: 6T Cell Full Layout
Transistor sizing
  M2 (pMOS) 4:3
  M1 (nMOS) 6:2
  M3 (nMOS) 4:2
All boundaries shared
38l H x 28l W
Reduced cap on bit lines
M3
M1
M2

## Slide 73: 6T Cell – Example Layout & Abutment
Vdd
Vss
Vss
Vdd
Vss
Vss
Vdd
B
B’
B’
B
B
4 x 4 array
Vdd
Vss
T3
T4
T1
T2
T5
T6
Vdd
Vss
T3
T4
T1
T2
T5
T6
Vdd
Vss
T3
T4
T1
T2
T5
T6
Vdd
Vss
T3
T4
T1
T2
T5
T6
Vdd
Vss
T3
T4
T1
T2
T5
T6
2 x 2 abutment

## Slide 74: 6T and 4T Cell Layouts
BIT
BIT!
GND
Vdd
Word
Line
T1
T2
T3
T4
R1
R2
VDD
GND
Q
Q
WL
BL
BL
T4
T3
T5
T6
T1
T2

## Slide 75: 6T - 4T Cell Comparison
6T cell
  Merits
    Faster
    Better Noise Immunity
    Low standby current
  Demerits
    Large size due to 6 transistors
4T cell
  Merits
    Smaller cell, only 4 transistors
    HR Poly stacked above transistors
  Demerits
    Additional process step due to HR poly
    Poor noise immunity
    Large standby current
    Thermal instability

## Slide 76: 6T vs 4T cell SNM

## Slide 77: Transistor Level View of Core
Precharge
Row Decode
Column Decode
Sense Amp

## Slide 78: SRAM, Putting it all together
2n rows, 2m * k columns
n + m address lines, k bits data width

## Slide 79: Hierarchical Array Architecture
Subblocks
1 / output bit
Select 1 column / subblock
1 sense amp / subblock

## Slide 80: Standalone SRAM Floorplan Example

## Slide 81: Divided bit-line structure

## Slide 82: SRAM Partitioning Partitioned Bitline

## Slide 83: SRAM Partitioning Divided Wordline Arch

## Slide 84: Partitioning summary
Partitioning involves a trade off between area, power and speed
For high speed designs, use short blocks(e.g 64 rows x 128 columns )
  Keep local bitline heights small
For low power designs use tall narrow blocks (e.g 256 rows x 64 columns)

## Slide 85: Address Transition Detection Provides Clock for Asynch RAMs

## Slide 86: Row Decoders
Collection of 2R complex logic gates organized in a regular, dense fashion
(N)AND decoder 9->512
  WL(0) /= !A8!A7!A6!A5!A4!A3!A2!A1!A0
  …
  WL(511) /= A8A7A6A5A4A3A2A1A0
NOR decoder 9->512
  WL(0) = !(A8+A7+A6+A5+A4+A3+A2+A1+A0)
  …
  WL(511) = !(!A8+!A7+!A6+!A5+!A4+!A3+!A2+!A1+!A0)

## Slide 87: A NAND decoder using 2-input pre-decoders

## Slide 88
A0
A1
A2
A3
A0/ A1/ A0 A1/ A0/ A1 A0 A1 A2/ A3/ A2 A3/ A2/ A3 A2 A3
… and so forth
R0/
R1/
R2/
Row Decoders (cont’d)

## Slide 89: Dynamic Decoders

## Slide 90: Dynamic NOR Row Decoder
Vdd
A0
!A0
A1
!A1
WL3
WL2
WL1
WL0
Precharge/
Notes: Dynamic 2-to-4 NOR decoder – precharge all outputs high, then GND inactive outputs - active “high” output signals
Note that signal goes through at most one fet (so constant propagation delay (in theory)) – some output wires have two parallel paths to GND
Also note, that the capacitance of the output wires goes linearly with the decoder size (linear grow in fet diffusion capacitance)

## Slide 91: Dynamic NAND Row Decoder
!A0
A0
!A1
A1
WL0
Precharge/
WL1
WL2
WL3
Back
Notes: Dynamic 2-to-4 NAND decoder – precharge all outputs high, then discharge active output - active “low” output signals
Must ensure that all input signals are low during precharge – else Vdd and GND connected!
Note that the number of fets goes linearly with the decoder size – 2-to-4 has two fets in series, 3-to-8 has 3 fets in series, etc.- so will be slower than the NOR implementation if the gate capacitance dominates diffusion capacitance

## Slide 92: Decoders
n:2n decoder consists of 2n n-input AND gates
  One needed for each row of memory
  Build AND from NAND or NOR gates
Make devices on address line minimal size
Scale devices on decoder O/P to drive word lines
Static CMOS Pseudo-nMOS

## Slide 93: Row Decoders

## Slide 94: Decoder Designs

## Slide 95: Decoder Layout
Decoders must be pitch-matched to SRAM cell
  Requires very skinny gates

## Slide 96: Large Decoders
For n > 4, NAND gates become slow
  Break large gates into multiple smaller gates

## Slide 97: Predecoding
  Group address bits in predecoder
  Saves area
  Same path effort

## Slide 98: Split Row Decoder
Address<6:0>
*7
*7
*8
*8
!(!A0!A1!A2)
. . .
!(A0A1A2)
!(!(!A0!A1!A2) + !(!A3!A4!A5) +!A6)
WL0
WL0
WL127
WL127
*128
*128
Notes: Since address decoders need to interface with the core array cells, pitch matching with the core storage array can be difficult.
Can improve pitch and improve speed by splitting the decoder into smaller pieces.
Propagation delay reduced by a factor of 4 (# of inputs halved) – squared since dependency between delay and fan-in; and the load on the vertical address lines halved (also reducing the delay)
Also reduced the number of transistors – e.g., for a 10 input decoder with a 4-bit predecoder has 1024*6 (row decoder) + 5*4*4 (predecoder) = 6,224 as compared to 11*1024 = 11,264 yielding a 55% reduction
Address bit predecoded; the 18 lines of predecoded values are clocked and routed across the 128 array of final decoders. Each final decoder taps into one signal from each of the three sets to perform the final level of decoders.
Note that final row drivers have to drive a very long and heavily loaded word line, so have to drive them carefully (see lecture 24 – positioned in the center of the array, replicating circuitry at each end, strapping cells, etc.)

## Slide 99: Sense Amplifier: Why?
Bit line cap significant for large array
  If each cell contributes 2fF,
    for 256 cells, 512fF plus wire cap
  Pull-down resistance is about 15K
  RC = 7.5ns! (assuming DV = Vdd)
Cannot easily change R, C, or Vdd, but can change DV i.e. smallest sensed voltage
  Can reliably sense DV as small as <50mV
Cell pull down
Xtor resistance
Cell current

## Slide 100: Sense Amplifiers
t
p
Cb
D
V
×
I
cell
----------------
=
make
D
V as small
as possible
small
large
Idea: Use Sense Amplifer
output
input
s.a.
small
transition

## Slide 101: Differential Sensing - SRAM
Diff.
Sense
Amp
BL
BL
SRAM cell i
x
x
y
y
D
D
V
DD
V
DD
WL
i
PC
EQ
V
DD
x
x
y
SE
V
DD
x
x
y
SE
V
DD
x
x
y
SE
(b) Doubled-ended Current Mirror Amplifier
y
(a) SRAM sensing scheme.
(c) Cross-Coupled Amplifier
M1
M2
M4
M3
M5

## Slide 102: Latch-Based Sense Amplifier

## Slide 103: Sense Amplifier
bit’
bit
word
sense
clk
isolation transistor
regenerative amplifier

## Slide 104: Clocked Sense Amp
Clocked sense amp saves power
Requires sense_clk after enough bitline swing
Isolation transistors cut off large bitline capacitance

## Slide 105: Alpha Differential Amplifier/Latch
sense
sense_out
V = Vdd
!sense_out
S3
S2
S1
S0
column decoder
sense
amplifier
N2
N3
N4
N5
P1
P2
P3
P4
N1
mux_out
sense
precharge
!mux_out
0->1
Pre -> Closed)
0->1
off->on
Notes: N2 and N4 sense the voltage change on the bit lines (gates are connected to the two bit lines coming from the column decoder)
N1 enables the SA by providing current to the two detection devices.
The cross-coupled inverter pair (P1/N3 and P2/N5) is used to amplify the detected voltage differential.
Finally, a set of inverters is used to buffer the output of the SA.
Operation begins with sense in low state. P3 and P4 precharge sense and !sense to Vdd and the bit lines gating N2 and N4 are precharged to Vdd. As the read begins one of the two input lines will begin to discharge and sense is asserted. This causes the pulldown N1 to turn on supplying current to the two legs of the SA.

## Slide 106: Sense Amp Waveforms
200mV
2.5V
1ns / div
bit
bit’
wordline
sense clk
sense clk
BIT
BIT’
wordline
begin precharging bit lines

## Slide 109: Sense Amp (Caveat)
For SRAM, one S/A for 4-8 columns
  after column mux
For DRAM, one S/A for every column
  for refresh!
Need to precharge S/A before opening isolation transistors
  To avoid discharging bit lines
  Requires 3 timing phases
  Typically self-timed
Notes: In the example waveform, we precharged S/A by opening isolation transistors (with wordline kept low). However, if wordline is high when isolation transistors open, then a bit line may be discharged prematurely.

## Slide 110: Write Driver Circuits

## Slide 111: Twisted Bitlines
Sense amplifiers also amplify noise
  Coupling noise is severe in modern processes
  Try to couple equally onto bit and bit_b
  Done by twisting bitlines

## Slide 112: Transposed-Bitline Architecture

## Slide 113
1
2
3
4
5
6
7

## Slide 114: Review of Memory Hierarchies
CPU
Cache
(SRAM)
Main Memory
(DRAM)
Virtual Memory
(Hard Disk)
Increasing Speed
Increasing Capacity
Physical Memory

## Slide 115: Who Cares About the Memory Hierarchy?
µProc
60%/yr.
(2X/1.5yr)
DRAM
9%/yr.
(2X/10 yrs)
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
Time
“Moore’s Law”
Processor-DRAM Memory Gap (latency)
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 116: Cache Memory Motivation
Processor speeds are increasing much faster than memory speeds
Memory speed matters
  Each instruction / data needs to be fetched from memory
  Loads, stores are a significant fraction of instructions
  Amdahl’s Law tells us that increasing processor performance without speeding up memory won’t help much overall
Locality of references
  Locations that are close together in the address space tend to get referenced close together in time (spatial locality)
  Tend to reference the same memory locations over and over again (temporal locality)

## Slide 117: Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality
Bad locality behavior

## Slide 118
4/25/2014
CS252-Fall’07
118
Caches
Caches exploit both types of predictability:
  Exploit temporal locality by remembering the contents of recently accessed locations.
  Exploit spatial locality by fetching blocks of data around recently accessed locations.

## Slide 119: Cache Memories
Relatively small SRAM memories located physically close to the processor
  SRAMs have low access times
  Physical proximity reduces wire delay
Similar in concept to virtual memory
  Keep commonly-accessed data in smaller, fast memory
Inclusion property
  Any data in a given level of the hierarchy must be contained in all levels below that in the hierarchy.
    Means that we never have to worry about whether we have space for data we need to evict from one level into a lower level

## Slide 120: Cache Operation
On memory access, look in the cache first
If the address we want is in the cache, complete the operation, usually in one cycle
If not, complete the operation using the main memory (many cycles)

## Slide 121: Performance of Memory Hierarchies
Basic Formula:
Tavg = Phit * Thit + Pmiss * Tmiss
Thit = time to complete the memory reference if we hit in a given level of the hierarchy
Tmiss = time to complete the memory reference if we miss and have to go down to the next level
Phit, Pmiss = Probabilities of hitting or missing in the level
  Phit is always 100% for the bottom level of the hierarchy

## Slide 122: Example 1
A memory system consists of a cache and a main memory. If it takes 1 cycle to complete a cache hit, and 100 cycles to complete a cache miss, what is the average memory access time if the hit rate in the cache is 97%?
Thit = 1 cycle
Tmiss = 100 cycles
Phit = .97
Pmiss = .03
Tavg = Phit * Thit + Pmiss * Tmiss = 0.97 * 1 + .03 * 100
= 3.97 cycles

## Slide 123: Describing Caches
We characterize a cache using 5 parameters
Access Time: Thit
Capacity: the total amount of data the cache can hold
  # of lines * line length
Line Length / Block size: The amount of data that gets moved into or out of the cache as a chunk
  Analogous to page size in virtual memory
What happens on a write?
Replacement Policy: What data is replaced on a miss?
Associativity: How many locations in the cache is a given address eligible to be placed in?
Unified, Instruction, Data: What type of data is kept in the cache?

## Slide 124: Capacity
In general, bigger is better
  The more data you can store in the cache, the less often you have to go out to the main memory
However, bigger caches tend to be slower
  Need to understand how both Thit and Phit change as you change the capacity of the cache.
  Declining return on investment as cache size goes up

## Slide 125: Cache Line Length
  Cache groups contiguous addresses into lines
  Lines almost always aligned on their size
  Caches fetch or write back an entire line of data on a miss
    Spatial Locality
Reading/Writing a Line
  Typically, takes much longer to fetch the first word of a line than subsequent words
    Page Mode memories
Tfetch = Tfirst + (line length / fetch width) * Tsubsequent

## Slide 126: What causes a MISS?
4/25/2014
CS252-Fall’07
126
Three Major Categories of Cache Misses:
  Compulsory Misses: first access to a block
  Capacity Misses: cache cannot contain all blocks needed to execute the program
  Conflict Misses: block replaced by another block and then later retrieved - (affects set assoc. or direct mapped caches)
    Nightmare Scenario: ping pong effect!

## Slide 127: Block Size and Spatial Locality
4/25/2014
CS252-Fall’07
127
Word3
Word0
Word1
Word2
Larger block size has distinct hardware advantages
  less tag overhead
  exploit fast burst transfers from DRAM
  exploit fast burst transfers over wide busses
What are the disadvantages of increasing block size?
block address offsetb
2b = block size a.k.a line size (in bytes)
Split CPU address
b bits
32-b bits
Tag
Block is unit of transfer between the cache and memory
4 word block, b=2
Fewer blocks => more conflicts. Can waste bandwidth.
Notes: CS252 S05
127
Larger block size will reduce compulsory misses (first miss to a block).
Larger blocks may increase conflict misses since the number of blocks
is smaller.

## Slide 128: Miss Rates Vs Block Size
1
K
B
8
K
B
1
6
K
B
6
4
K
B
2
5
6
K
B
2
5
6
4
0
%
3
5
%
3
0
%
2
5
%
2
0
%
1
5
%
1
0
%
5
%
0
%
M
i
s
s
r
a
t
e
6
4
1
6
4
B
l
o
c
k
s
i
z
e
(
b
y
t
e
s
)
Cache size

## Slide 129: Hit Rate isn’t Everything
Average access time is better performance indicator than hit rate
Tavg = Phit * Thit + Pmiss * Tmiss
Tmiss = Tfetch = Tfirst + (line length / fetch width) * Tsubsequent
Trade-off: Increasing line length usually increases hit rate, but also increases fetch time
  As lines get bigger, increase in fetch time starts to outweigh increase in miss rate

## Slide 130: Block Size Tradeoff
In general, larger block size take advantage of spatial locality BUT:
  Larger block size means larger miss penalty:
    Takes longer time to fill up the block
  If block size is too big relative to cache size, miss rate will go up
    Too few cache blocks
In general, Average Access Time:
  = Hit Time x (1 - Miss Rate) + Miss Penalty x Miss Rate
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Block Size
Notes: As I said earlier, block size is a tradeoff. In general, larger block size will reduce the miss rate because it take advantage of spatial locality.
But remember, miss rate NOT the only cache performance metrics. You also have to worry about miss penalty.
As you increase the block size, your miss penalty will go up because as the block gets larger, it will take you longer to fill up the block.
Even if you look at miss rate by itself, which you should NOT, bigger block size does not always win. As you increase the block size, assuming keeping cache size constant, your miss rate will drop off rapidly at the beginning due to spatial locality.
However, once you pass certain point, your miss rate actually goes up.
As a result of these two curves, the Average Access Time (point to equation), which is really the more important performance metric than the miss rate, will go down initially because the miss rate is dropping much faster than the increase in miss penalty.
But eventually, as you keep on increasing the block size, the average access time can go up rapidly because not only is the miss penalty is increasing, the miss rate is increasing as well.
Let me show you why your miss rate may go up as you increase the block size by another extreme example.
+3 = 33 min. (Y:13)

## Slide 131: Basics of caches
How do we determine if the data is in the cache?
If data is in the cache, how is it found?
We only have information on:
  address of data
  how the cache is organised
Direct mapped cache:
  the data can only be at a specific place

## Slide 132: Data Address is used to organise cache storage strategy
Word is organised by byte bits
Block is organised by bits denoting the word
Location in cache is indexed by row
Tag is identification of a block in a cache row
Tag
Index
Block
Byte
Word address bits fields

## Slide 133: Example 24 bit address with 8 byte block and 2048 blocks in cache of 16384 bytes

## Slide 134: Where can a block be placed ?
Block 12 placed in 8 block cache:
  Fully associative, direct mapped, 2-way set associative
  S.A. Mapping = Block Number Modulo Number Sets
0 1 2 3 4 5 6 7
Block
no.
Fully associative:
block 12 can go anywhere
0 1 2 3 4 5 6 7
Block
no.
Direct mapped:
block 12 can go only into block 4 (12 mod 8)
0 1 2 3 4 5 6 7
Block
no.
Set associative:
block 12 can go anywhere in set 0 (12 mod 4)
Set
0
Set
1
Set
2
Set
3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
Block-frame address
1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3
Block
no.

## Slide 135: How is a block found if it is in the upper level?
Direct indexing (using index and block offset), tag compares, or combination
Increasing associativity shrinks index, expands tag
Block
offset
Block Address
Tag
Index

## Slide 136: Contents of a direct mapped cache
Data == Cached block
TAG == Most significant bits of cached block address that identify the block in that cache row from other blocks that map to that same row
VALID == Flag bit to indicate the cache content is valid

## Slide 137: Direct cache
Separate address into fields:
Byte offset in word
Index for row of cache
Tag identifier of block
A
d
d
r
e
s
s
(
s
h
o
w
i
n
g
b
i
t
p
o
s
i
t
i
o
n
s
)
2
0
1
0
B
y
t
e
o
f
f
s
e
t
V
a
l
i
d
T
a
g
D
a
t
a
I
n
d
e
x
0
1
2
1
0
2
1
1
0
2
2
1
0
2
3
T
a
g
I
n
d
e
x
H
i
t
D
a
t
a
2
0
3
2
3
1
3
0
1
3
1
2
1
1
2
1
0
ADDRESS
Cache of 2^n words, a block being a 4 byte word, has 2^n*(63-n) bits for 32 bit address
#rows=2^n
#bits/row=32+32-2-n+1=63-n

## Slide 138: Example: 1 KB Direct Mapped Cache with 32 Byte Blocks
For a 2 ** N byte cache:
  The uppermost (32 - N) bits are always the Cache Tag
  The lowest M bits are the Byte Select (Block Size = 2 ** M)
Cache Index
0
1
2
3
:
Cache Data
Byte 0
0
4
31
:
Cache Tag
Example: 0x50
Ex: 0x01
0x50
Stored as part
of the cache “state”
Valid Bit
:
31
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
Cache Tag
Byte Select
Ex: 0x00
9
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 KB direct mapped cache with block size equals to 32 bytes.
In other words, each block associated with the cache tag will have 32 bytes in it (Row 1).
With Block Size equals to 32 bytes, the 5 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K byte, the upper 32 minus 10 bits, or 22 bits of the address will be stored as cache tag.
The rest of the address bits in the middle, that is bit 5 through 9, will be used as Cache Index to select the proper cache entry.
+2 = 30 min. (Y:10)

## Slide 139: Extreme Example: single big line
Cache Size = 4 bytes Block Size = 4 bytes
  Only ONE entry in the cache
If an item is accessed, likely that it will be accessed again soon
  But it is unlikely that it will be accessed again immediately!!!
  The next access will likely be a miss again
    Continually loading data into the cache but discard (force out) them before they are used again
    Worst nightmare of a cache designer: Ping Pong Effect
Conflict Misses are misses caused by:
  Different memory locations mapped to the same cache index
    Solution 1: make the cache size bigger
    Solution 2: Multiple entries for the same Cache Index
0
Cache Data
Valid Bit
Byte 0
Byte 1
Byte 3
Cache Tag
Byte 2
Notes: Let’s go back to our 4-byte direct mapped cache and increase its block size to 4 byte. Now we end up have one cache entries instead of 4 entries.
What do you think this will do to the miss rate? Well the miss rate probably will go to hell. It is true that if an item is accessed, it is likely that it will be accessed again soon.
But probably NOT as soon as the very next access so the next access will cause a miss again. So what we will end up is loading data into the cache but the data will be forced out by another cache miss before we have a chance to use it again.
This is called the ping pong effect: the data is acting like a ping pong ball bouncing in and out of the cache. It is one of the nightmares scenarios cache designer hope never happens.
We also defined a term for this type of cache miss, cache miss caused by different memory location mapped to the same cache index. It is called Conflict miss.
There are two solutions we can use to reduce the conflict miss. The first one is to increase the cache size.
The second one is to increase the number of cache entries per cache index. Let me show you what I mean.
+2 = 35 min. (Y:15)

## Slide 140: Another Extreme Example: Fully Associative
Fully Associative Cache, N blocks of 32 bytes each
  Forget about the Cache Index
  Compare the Cache Tags of all cache entries in parallel
  Example: Block Size = 32 Byte blocks, we need N 27-bit comparators
:
Cache Data
Byte 0
0
4
31
:
Cache Tag (27 bits long)
Valid Bit
:
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Cache Tag
Byte Select
Ex: 0x01
X
X
X
X
X
Notes: While the direct mapped cache is on the simple end of the cache design spectrum, the fully associative cache is on the most complex end.
It is the N-way set associative cache carried to the extreme where N in this case is set to the number of cache entries in the cache.
In other words, we don’t even bother to use any address bits as the cache index.
We just store all the upper bits of the address (except Byte select) that is associated with the cache block as the cache tag and have one comparator for every entry.
The address is sent to all entries at once and compared in parallel and only the one that matches are sent to the output. This is called an associative lookup.
Needless to say, it is very hardware intensive. Usually, fully associative cache is limited to 64 or less entries.
Since we are not doing any mapping with the cache index, we will never push any other item out of the cache because multiple memory locations map to the same cache location.
Therefore, by definition, conflict miss is zero for a fully associative cache. This, however, does not mean the overall miss rate will be zero.
Assume we have 64 entries here. The first 64 items we accessed can fit in.
But when we try to bring in the 65th item, we will need to throw one of them out to make room for the new item. This bring us to the third type of cache misses: Capacity Miss.
+3 = 41 min. (Y:21)

## Slide 141: A Two-way Set Associative Cache
N-way set associative: N entries for each Cache Index
  N direct mapped caches operates in parallel
Example: Two-way set associative cache
  Cache Index selects a “set” from the cache
  The two tags in the set are compared in parallel
  Data is selected based on the tag result
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Index
Mux
0
1
Sel1
Sel0
Cache Block
Compare
Adr Tag
Compare
OR
Hit
Notes: This is called a 2-way set associative cache because there are two cache entries for each cache index. Essentially, you have two direct mapped cache works in parallel.
This is how it works: the cache index selects a set from the cache. The two tags in the set are compared in parallel with the upper bits of the memory address.
If neither tag matches the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data on the side where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 142: DRAM in a nutshell
Based on capacitive (non-regenerative) storage
Highest density (Gb/cm2)
Large external memory (Gb) or embedded DRAM for image, graphics, multimedia…
Needs periodic refresh -> overhead, slower

## Slide 144: Classical DRAM Organization (square)
r
o
w
d
e
c
o
d
e
r
row
address
Column Selector &
I/O Circuits
Column
Address
data
RAM Cell
Array
word (row) select
bit (data) lines
Row and Column Address together:
  Select 1 bit a time
Each intersection represents
a 1-T DRAM Cell
Notes: Similar to SRAM, DRAM is organized into rows and columns.
But unlike SRAM, which allows you to read an entire row out at a time at a word, classical DRAM only allows you read out one-bit at time time.
The reason for this is to save power as well as area. Remember now the DRAM cell is very small we have a lot of them across horizontally.
So it will be very difficult to build a Sense Amplifier for each column due to the area constraint not to mention having a sense amplifier per column will consume a lot of power.
You select the bit you want to read or write by supplying a Row and then a Column address.
Similar to SRAM, each row control line is referred to as the word line and each vertical data line is referred to as the bit line.
+2 = 57 min. (Y:37)

## Slide 145: DRAM logical organization (4 Mbit)

## Slide 146: DRAM physical organization (4 Mbit,x16)

## Slide 147: Memory Systems
DRAM
2^n x 1
chip
DRAM
Controller
address
Memory
Timing
Controller
Bus Drivers
n
n/2
w
Tc = Tcycle + Tcontroller + Tdriver

## Slide 148: Logic Diagram of a Typical DRAM
A
D
OE_L
256K x 8
DRAM
9
8
WE_L
Control Signals (RAS_L, CAS_L, WE_L, OE_L) are all active low
Din and Dout are combined (D):
  WE_L is asserted (Low), OE_L is disasserted (High)
    D serves as the data input pin
  WE_L is disasserted (High), OE_L is asserted (Low)
    D is the data output pin
Row and column addresses share the same pins (A)
  RAS_L goes low: Pins A are latched in as row address
  CAS_L goes low: Pins A are latched in as column address
  RAS/CAS edge-sensitive
CAS_L
RAS_L
Notes: Here is the logic diagram of a typical DRAM.
In order to save pins, Din and Dout are combined into a set of bidirectional pins so you need two pins Write Enable and Output Enable to control the D pins’ directions.
In order to further save pins, the row and column addresses share one set of pins, pins A whose function is controlled by the Row Address Strobe and Column Address Strobe pins both of which are active low.
Whenever the Row Address Strobe makes a high to low transition, the value on the A pins are latched in as Row address.
Whenever the Column Address Strobe makes a high to low transition, the value on the A pins are latched in as Column address.
+2 = 60 min. (Y:40)

## Slide 149: DRAM Operations
Write
  Charge bitline HIGH or LOW and set wordline HIGH
Read
  Bit line is precharged to a voltage halfway between HIGH and LOW, and then the word line is set HIGH.
  Depending on the charge in the cap, the precharged bitline is pulled slightly higher or lower.
  Sense Amp Detects change
Explains why Cap can’t shrink
  Need to sufficiently drive bitline
  Increase density => increase parasitic capacitance
Word Line
Bit Line
C
Sense Amp
. . .

## Slide 150: Key DRAM Timing Parameters
tRAC: minimum time from RAS line falling to the valid data output.
  Quoted as the speed of a DRAM
  A fast 4Mb DRAM tRAC = 60 ns
tRC: minimum time from the start of one row access to the start of the next.
  tRC = 110 ns for a 4Mbit DRAM with a tRAC of 60 ns
tCAC: minimum time from CAS line falling to valid data output.
  15 ns for a 4Mbit DRAM with a tRAC of 60 ns
tPC: minimum time from the start of one column access to the start of the next.
  35 ns for a 4Mbit DRAM with a tRAC of 60 ns

## Slide 151: DRAM Read Timing
A
D
OE_L
256K x 8
DRAM
9
8
WE_L
CAS_L
RAS_L
OE_L
A
Row Address
WE_L
Junk
Read Access
Time
Output Enable
Delay
CAS_L
RAS_L
Col Address
Row Address
Junk
Col Address
D
High Z
Data Out
DRAM Read Cycle Time
Early Read Cycle: OE_L asserted before CAS_L
Late Read Cycle: OE_L asserted after CAS_L
Every DRAM access begins at:
  The assertion of the RAS_L
  2 ways to read: early or late v. CAS
Junk
Data Out
High Z
Notes: Similar to DRAM write, DRAM read can also be a Early read or a Late read.
In the Early Read Cycle, Output Enable is asserted before CAS is asserted so the data lines will contain valid data one Read access time after the CAS line has gone low.
In the Late Read cycle, Output Enable is asserted after CAS is asserted so the data will not be available on the data lines until one read access time after OE is asserted.
Once again, notice that the RAS line has to remain asserted during the entire time. The DRAM read cycle time is defined as the time between the two RAS pulse.
Notice that the DRAM read cycle time is much longer than the read access time.
Q: RAS & CAS at same time? Yes, both must be low
+2 = 65 min. (Y:45)

## Slide 152: DRAM Write Timing
A
D
OE_L
256K x 8
DRAM
9
8
WE_L
CAS_L
RAS_L
WE_L
A
Row Address
OE_L
Junk
WR Access Time
WR Access Time
CAS_L
RAS_L
Col Address
Row Address
Junk
Col Address
D
Junk
Junk
Data In
Data In
Junk
DRAM WR Cycle Time
Early Wr Cycle: WE_L asserted before CAS_L
Late Wr Cycle: WE_L asserted after CAS_L
Every DRAM access begins at:
  The assertion of the RAS_L
  2 ways to write: early or late v. CAS
Notes: Let me show you an example. Here we are performing two write operation to the DRAM.
Setup/hold times in colar bars
Remember, this is very important. All DRAM access start with the assertion of the RAS line.
When the RAS_L line go low, the address lines are latched in as row address. This is followed by the CAS_L line going low to latch in the column address.
Of course, there will be certain setup and hold time requirements for the address as well as data as highlighted here.
Since the Write Enable line is already asserted before CAS is asserted, write will occur shortly after the column address is latched in. This is referred to as the Early Write Cycle.
This is different from the 2nd example I showed here where the Write Enable signal comes AFTER the assertion of CAS. This is referred to as a Later Write cycle.
Notice that in the early write cycle, the width of the CAS line, which you as a logic designer can and should control, must be as long as the memory’s write access time.
On the other hand, in the later write cycle, the width of the Write Enable pulse must be as wide as the WR Access Time.
Also notice that the RAS line has to remain asserted (low) during the entire access cycle.
The DRAM write cycle time is defined as the time between the two RAS pulse and is much longer than the DRAM write access time.
+3 = 63 min. (Y:43)

## Slide 153: Key DRAM Timing Parameters
tRAC: minimum time from RAS line falling to the valid data output.
  Quoted as the speed of a DRAM
  A fast 4Mb DRAM tRAC = 60 ns
tRC: minimum time from the start of one row access to the start of the next.
  tRC = 110 ns for a 4Mbit DRAM with a tRAC of 60 ns
tCAC: minimum time from CAS line falling to valid data output.
  15 ns for a 4Mbit DRAM with a tRAC of 60 ns
tPC: minimum time from the start of one column access to the start of the next.
  35 ns for a 4Mbit DRAM with a tRAC of 60 ns

## Slide 154: DRAM Performance
A 60 ns (tRAC) DRAM can
  perform a row access only every 110 ns (tRC)
  perform column access (tCAC) in 15 ns, but time between column accesses is at least 35 ns (tPC).
    In practice, external address delays and turning around buses make it 40 to 50 ns
Add the time to drive the addresses off the microprocessor & the memory controller overhead.
  Drive parallel DRAMs, external memory controller, bus to turn around, SIMM module, pins…
  180 ns to 250 ns latency from processor to memory is good for a “60 ns” (tRAC) DRAM

## Slide 155: DRAM Performance
DRAM (Read/Write) Cycle Time >> DRAM (Read/Write) Access Time
  ­ 2:1; why?
DRAM (Read/Write) Cycle Time :
  How frequent can you initiate an access?
DRAM (Read/Write) Access Time:
  How quickly will you get what you want once you initiate an access?
DRAM Bandwidth Limitation:
  Limited by Cycle Time
Time
Access Time
Cycle Time

## Slide 156: Refreshing Overhead
Leakage :
  junction leakage exponential with temp!
  2…8 msec @ 800 C
  Decreases noise margin, destroys info
All columns in a selected row are refreshed when read
  Count through all row addresses once per 3 msec. (no write possible then)
Overhead @ 10nsec read time for 8192(rows)*8192(cols)=64Mb:
  8192 (rows) *1e-8/3e-3= 2.7%
Requires additional refresh counter and I/O control

## Slide 157: 1-Transistor Memory Cell (DRAM)
Write:
  1. Drive bit line
  2.. Select row
Read:
  1. Precharge bit line
  2.. Select row
  3. Cell and bit line share charges
    Very small voltage changes on the bit line
  4. Sense (fancy sense amp)
    Can detect changes of ~1 million electrons
  5. Write: restore the value
Refresh
  1. Just do a dummy read to every cell.
row select
bit

## Slide 158: DRAM architecture

## Slide 159: Cell read

## Slide 160: 16k DRAM (Double Poly Cell)
MostekMK4116, introduced 1977
Address multiplex
Page mode
NMOS, 2P1M
Vdd=12v, Vcc=5v, Vbb=-5v (Vss=0v)
Vdd-Vt precharge, dynamic sensing

## Slide 161: 1M DRAM
Triple poly Planar cell, 3P1M
  poly1 -gate, W/L
  poly2 –plate
  poly3 (polycide) -B/L
  metal -W/L strap
Vdd/2 bitline reference, Vdd/2 cell plate

## Slide 162: 4M DRAM
3D stacked or trench cell
CMOS 4P1M
x16 introduced
Self Refresh
Build cell in vertical dimension -shrink area while maintaining 30fF cell capacitance

## Slide 164: Stacked-Capacitor Cells
Poly plate
Hitachi 64Mbit DRAM Cross Section
Samsung 64Mbit DRAM Cross Section
COB=Capacitor over bit

## Slide 165: Evolution of DRAM cell structures

## Slide 166: Buried Strap Trench Cell

## Slide 167: Process Flow of BEST Cell DRAM
· Array Buried N-Well
· Storage Trench Formation
· Node Dielectric (6nm TEQ.)
· Buried Strap Formation
· Shallow Trench Isolation Formation
· N- and P-Well Implants
· Gate Oxidation (8nm)
· Gate Conductor (N+ poly / WSi)
· Junction Implants
· Insulator Deposition and Planarization
· Contact formation
· Bitline (Metal 0) formation
· Via 1 / Metal 1 formation
· Via 2 / Metal 2 formation
Shallow Trench Isolation -> Replaces LOCOS isolation -> saves area by eliminating Bird’s Beak

## Slide 168: Sense Amplifier

## Slide 170: Example of Mitsubishi DRAM column

## Slide 171: On-chip Voltage Generators
Power supplies
  for logic and memory
precharge voltage
  e.g VDD/2 for DRAM Bitline .
backgate bias
  reduce leakage
WL select overdrive (DRAM)

## Slide 172: Charge Pump Operating Principle
+Vin
Vin
~ +Vin
+Vin
Vin
dV
dV
Vo
Vin = dV – Vin + dV +Vo
Vo = 2*Vin + 2*dV ~ 2*Vin
Charge Phase
Discharge Phase

## Slide 173: Voltage Booster for WL
Cf
CL
Vhi
dV
VGG=Vhi
CL
Cf
Vcf ~ Vhi
Vhi
Vcf(0) ~ Vhi
+
VGG ~ Vhi + Vhi
d

## Slide 174: Body Effect Model
fs = surface potential at threshold
  Depends on doping level NA
  And intrinsic carrier concentration ni
g = body effect coefficient

## Slide 175: Backgate bias generation
Use charge pump
Backgate bias:
Increases Vt -> reduces leakage
• reduces Cj of nMOST when applied to p-well (triple well process!),
smaller Cj -> smaller Cb → larger readout ΔV

## Slide 176: Vdd / 2 Generation
2v
1v
1v
0.5v
0.5v
1.5v
~1v
0.5v
1v
Vtn = |Vtp|~0.5v
uN = 2 uP

## Slide 177: DRAM technological requirements
Unlike SRAM : large Cb must be charged by small sense FF. This is slow.
  Make Cb small: backbias junction cap., limit blocksize,
  Backbias generator required. Triple well.
Prevent threshold loss in wl pass: VG > Vccs+VTn
  Requires another voltage generator on chip
Requires VTnwl> Vtnlogic and thus thicker oxide than logic
  Better dynamic data retention as there is less subthreshold loss.
  DRAM Process unlike Logic process!
Must create “large” Cs (10..30fF) in smallest possible area
  (-> 2 poly-> trench cap -> stacked cap)

## Slide 178: Refreshing Overhead
Leakage :
  junction leakage exponential with temp!
  2…8 msec @ 800 C
  Decreases noise margin, destroys info
All columns in a selected row are refreshed when read
  Count through all row addresses once per 3 msec. (no write possible then)
Overhead @ 10nsec read time for 8192*8192=64Mb:
  8192*1e-8/3e-3= 2.7%
Requires additional refresh counter and I/O control

## Slide 179
Dummy Cell on BL’

## Slide 180
Differential Operation in DRAM with Vdd/2 precharge
• Sense amplifier works only for differential signal on B and B’ and rejects interference signals
• In differential circuit
Each bit line split into two identical halves
Each half-line connected to half of cells in column and additional dummy cell with storage capacitance Cd=Cs
– Upon selecting word line on the left side, dummy right cell (controlled by clk’d) is selected and vv.
Dummy cell is other half of differential DRAM cell
• Operation of differential circuit
  Two halves of Bitline Bk and Cd of two dummy cells precharged to VDD/2
  Upon selection of word line, appropriate dummy cell activated by rising clkd (clk’d)
  Voltage increment (above VDD/2) on half-line connected to selected cell
  dV(1) when 1 stored in cell, dV(0) otherwise

## Slide 181: DRAM technological requirements
Unlike SRAM : large Cb must be charged by small sense FF. This is slow.
  Make Cb small: backbias junction cap., limit blocksize,
  Backbias generator required. Triple well.
Prevent threshold loss in wl pass: VG > Vccs+VTn
  Requires another voltage generator on chip
Requires VTnwl> Vtnlogic and thus thicker oxide than logic
  Better dynamic data retention as there is less subthreshold loss.
  DRAM Process unlike Logic process!
Must create “large” Cs (10..30fF) in smallest possible area
  (-> 2 poly-> trench cap -> stacked cap)

## Slide 182: Refreshing Overhead
Leakage :
  junction leakage exponential with temp!
  2…8 msec @ 800 C
  Decreases noise margin, destroys info
All columns in a selected row are refreshed when read
  Count through all row addresses once per 3 msec. (no write possible then)
Overhead @ 10nsec read time for 8192*8192=64Mb:
  8192*1e-8/3e-3= 2.7%
Requires additional refresh counter and I/O control

## Slide 183
Dummy Cell on BL’

## Slide 184
Differential Operation in DRAM with Vdd/2 precharge
• Sense amplifier works only for differential signal on B and B’ and rejects interference signals
• In differential circuit
Each bit line split into two identical halves
Each half-line connected to half of cells in column and additional dummy cell with storage capacitance Cd=Cs
– Upon selecting word line on the left side, dummy right cell (controlled by clk’d) is selected and vv.
Dummy cell is other half of differential DRAM cell
• Operation of differential circuit
  Two halves of Bitline Bk and Cd of two dummy cells precharged to VDD/2
  Upon selection of word line, appropriate dummy cell activated by rising clkd (clk’d)
  Voltage increment (above VDD/2) on half-line connected to selected cell
  dV(1) when 1 stored in cell, dV(0) otherwise

## Slide 185
½ Bitline
½ Bitline
Wordline
Vdd/2
precharge
Vdd/2
precharge
Dummy cells
Additional wire &
Contact in cell

## Slide 186: Alternative Sensing Strategy Decreasing Cdummy
Convert to differential sense
  Create a reference in an identical structure
Needs
  A method of generating ½ signal swing of bit line
Operation:
  Dummy cell is ½ C
  active wordline and dummy wordline on opposite sides of sense amp.
  Amplify difference
So Small Cs small swing, Large Cb small swing
BL’
BL
Overhead of fabricating C/2

## Slide 187: Alternative Sensing Strategy Increasing Cbitline on Dummy side
SA outputs D and D pre-charged to VDD through Q1, Q2 (Pr=1)
•reference capacitor, Cdummy, connected to a pair of matched bit lines and is at 0V (Pr=0)
•parasitic cap Cp2 on BL’ is ~ 2 Cp1 on BL,
sets up a differential voltage LHS vs. RHS due to rise time difference
SA outputs (D, D) become charged, with a small difference LHS vs. RHS
Regenerative Action of Latch
Data
Dummy
Double Bitline

## Slide 190: Cell Array and Circuits
1 Transistor 1 Capacitor Cell
  Array Example
Major Circuits
  ・Sense amplifier
  ・Dynamic Row Decoder
  ・Wordline Driver
Other interesting circuits ・
  Data bus amplifier ・
  Voltage Regulator
  Reference generator
  Redundancy technique
  High speed I/O circuits

## Slide 191: Standard DRAM Array Design Example

## Slide 192
BL direction (col)
WL direction
(row)
64K cells
(256x256)
1M cells =
64Kx16
Global WL decode + drivers
Local WL
Decode
Column predecode
SA+col mux

## Slide 193: DRAM Array Example (cont’d)
512K Array Nmat=16 ( 256 WL x 2048 SA)
Interleaved S／A & Hierarchical Row Decoder/Driver
(shared bit lines are not shown)
2048 SA (Lower + Upper)
256
256x256
64

## Slide 194: DRAM Performance
Ratio of DRAM (Read/Write) Cycle Time to DRAM (Read/Write) Access Time
  ­ 2:1; why?
DRAM (Read/Write) Cycle Time :
  How frequent can you initiate an access?
DRAM (Read/Write) Access Time:
  How quickly will you get what you want once you initiate an access?
DRAM Bandwidth Limitation:
  Limited by Cycle Time
Time
Access Time
Cycle Time

## Slide 204: Fast Memory Systems: DRAM specific
Multiple column accesses per RAS: page mode
  DRAM buffers a row of bits inside the DRAM for column access (e.g., 16 Kbits row for 64 Mbits DRAM)
  Allow repeated column access without another row access
  64 Mbit DRAM: cycle time = 90 ns, optimized access = 25 ns
New DRAMs:
  Synchronous DRAM: Provide a clock signal to DRAM, transfer synchronous to system clock
  RAMBUS: startup company; reinvent DRAM interface
    Each chip a module vs. slice of memory
    Short bus between CPU and chips
    Does own refresh
    Variable amount of data returned
    1 byte / 2 ns (500 MB/s per chip)

## Slide 205: Page Mode DRAM: Motivation
Regular DRAM Organization:
  N rows x N column x M-bit
  Read & Write M-bit at a time
  Each M-bit access requires a RAS / CAS cycle
Fast Page Mode DRAM
  N x M “register” to save a row
A
Row Address
Junk
CAS_L
RAS_L
Col Address
Row Address
Junk
Col Address
1st M-bit Access
2nd M-bit Access
N rows
N cols
DRAM
M bits
Row
Address
Column
Address
M-bit Output

## Slide 206: Fast Page Mode Operation
Fast Page Mode DRAM
  N x M “SRAM” to save a row
After a row is read into the register
  Only CAS is needed to access other M-bit blocks on that row
  RAS_L remains asserted while CAS_L is toggled
A
Row Address
CAS_L
RAS_L
Col Address
Col Address
1st M-bit Access
N rows
N cols
DRAM
Column
Address
M-bit Output
M bits
N x M “SRAM”
Row
Address
Col Address
Col Address
2nd M-bit
3rd M-bit
4th M-bit

## Slide 207: Page Mode DRAM Bandwidth Example
Page Mode DRAM Example:
  16 bits x 1M DRAM chips (4 nos) in 64-bit module (8 MB module)
  60 ns RAS+CAS access time; 25 ns CAS access time
  Latency to first access=60 ns Latency to subsequent accesses=25 ns
  110 ns read/write cycle time; 40 ns page mode access time ; 256 words (64 bits each) per page
Bandwidth takes into account 110 ns first cycle, 40 ns for CAS cycles
Bandwidth for one word = 8 bytes / 110 ns = 69.35 MB/sec
Bandwidth for two words = 16 bytes / (110+40 ns) = 101.73 MB/sec
Peak bandwidth = 8 bytes / 40 ns = 190.73 MB/sec
Maximum sustained bandwidth = (256 words * 8 bytes) / ( 110ns + 256*40ns) = 188.71 MB/sec

## Slide 208: DRAM Memory Systems
DRAM
2^n x 1
chip
DRAM
Controller
address
Memory
Timing
Controller
Bus Drivers
n
n/2
w
Tc = Tcycle + Tcontroller + Tdriver

## Slide 209: DRAM Performance
Simple:
  CPU, Cache, Bus, Memory same width (32 bits)
Interleaved:
  CPU, Cache, Bus 1 word: Memory N Modules (4 Modules); example is word interleaved
Wide:
  CPU/Mux 1 word; Mux/Cache, Bus, Memory N words (Alpha: 64 bits & 256 bits)

## Slide 210: Increasing Bandwidth - Interleaving
Access Pattern without Interleaving:
Start Access for D1
CPU
Memory
Start Access for D2
D1 available
Access Pattern with 4-way Interleaving:
Access Bank 0
Access Bank 1
Access Bank 2
Access Bank 3
We can Access Bank 0 again
CPU
Memory
Bank 1
Memory
Bank 0
Memory
Bank 3
Memory
Bank 2

## Slide 219: Non Volatile Memories

## Slide 220: Non Volatile memory types

## Slide 221: Read-Only Memory Cells
WL
BL
WL
BL
1
WL
BL
WL
BL
WL
BL
0
VDD
WL
BL
GND
Diode ROM
MOS ROM 1
MOS ROM 2
Absence/presence of transistor determines 1/0 or v.v.

## Slide 222: MOS NOR ROM
WL
[0]
GND
BL
[0]
WL
[1]
WL
[2]
WL
[3]
V
DD
BL
[1]
Pull-up devices
BL
[2]
BL
[3]
GND
Presence of transistor at data bit = 0

## Slide 223: Precharged MOS NOR ROM
PMOS precharge device can be made as large as necessary,
but clock driver becomes harder to design.
WL
[0]
GND
BL
[0]
WL
[1]
WL
[2]
WL
[3]
V
DD
BL
[1]
Precharge devices
BL
[2]
BL
[3]
GND
pre
f
Presence of transistor at data bit = 0

## Slide 224: MOS NOR ROM Layout
BL[0]
BL[1]
BL[2]
BL[3]

## Slide 225: MOS NOR ROM Layout
Presence of Implant == Absence of transistor

## Slide 226: MOS NAND ROM
All word lines high by default with exception of selected row
/WL
[0]
/WL
[1]
/WL
[2]
/WL
[3]
V
DD
Pull-up devices
BL
[3]
BL
[2]
BL
[1]
BL
[0]
WL are active low
Presence of transistor at data bit = 1

## Slide 227: MOS NAND ROM Layout
BL[0]
BL[1]
BL[2]
BL[3]
Presence of Implant == Absence of transistor
Implant fixed by mask.
Can it be made dynamic??

## Slide 229: Non-Volatile Memories The Floating-gate transistor (FAMOS)
Floating gate
Source
Substrate
Gate
Drain
n
+
n
+_
p
t
ox
t
ox
Device cross-section
Schematic symbol
G
S
D

## Slide 230: Floating-Gate Transistor Programming
0 V
5 V
0 V
D
S
Removing programming
voltage leaves charge trapped
5 V
2.5 V
5 V
D
S
Programming results in
higher
V
T
.
20 V
10 V
5 V
20 V
D
S
Avalanche injection

## Slide 231: Floating gate Transistor
Cfs
Cfd
Cpp
Cf
Ctot = Cpp + Cf
Cox lower,so slope reduced
Cox lower, Vt higer,
curve shifts right
DVt = Qfg / Cpp
Qfg !=0, Vt increases further
Curve shifts further

## Slide 232: Sensing Thresholds
Multi Bit / Multi Level Cell

## Slide 234: Floating Gate Memory Cells
EPROM
  UV erasable
EEPROM
  Electrically erasable, can be read/written/erased/ on byte/word basis
Flash memory
  Also called flash EEPROM
  Can be cleared to 0/1 on a block basis
  Bytes can be written inside block
    By flipping some of the cleared cells

## Slide 235: Floating Gate Program/Erase

## Slide 236: Basic Floating-Gate Transistor: Weight Change Mechanisms
pFET Floating-Gate Synapse
Change floating-gate charge
using:
Tunneling Current
Injection Current
Notes: The third term now shows up as an adaptive scale factor in the bias current, as well as an adaptive scale factor modulating the transconductance.
So now, how do we adapt the charge on the floating-gate if there are no conductive paths connecting it to anything?
We take advantage of two processes from the device physics: electron tunneling, which allows us to add charge to the floating-gate, and hot-electron injection which allows us to remove charge from the floating-gate.
These two processes are described by currents dependent on tunneling and injection.
For continuous-time adaptation, we fix the tunneling current to a bias value, and allow the injection current to vary around this operating point.
The dynamics of the floating-gate voltage can be determined by writing KCL at the floating-node. We will separate this differential equation into fast and slow timescales such that we can ignore Vg dot and Vd dot...

## Slide 237: Modify Floating-gate Information
Information storage
Three methods of modification
  UV photo injection
  Electron tunneling
  Hot-electron injection
Access Gate

## Slide 238: Modify Floating-gate Information
Methods for changing information
  UV photo injection
  Electron tunneling
  Hot-electron injection
Access Gate
Requires costly package
Programming time is lengthy
Difficult to selectively program
Perfect for normalizing arrays.
Notes: Examine the methods of charge change and generally exclude UV injection due to costs.

## Slide 240: Modify Floating-gate Information
Methods for changing information
  UV photo injection
  Electron tunneling
  Hot-electron injection
Access Gate
Fowler-Nordheim Tunneling
field-assisted electron tunneling
electrons are waves too!
Notes: Examine the methods of charge change and generally exclude UV injection due to costs.

## Slide 241: Transistor Leakage Mechanisms
1. pn Reverse Bias Current
2. Subthreshold (Weak Inversion)
3. Drain Induced Barrier Lowering
4. Gate Induced Drain Leakage
5. Punchthrough
6. Narrow Width Effect
7. Hot Carrier Injection
8. Gate Oxide Tunneling
Utilised to
Prog/Erase
EEPROMs
Rev biased
Junc Band to
Band Tunneling
(BTBT)

## Slide 242: Gate Oxide Tunneling
Fowler-Nordheim tunneling
  high electric field across thin gate oxide layer
In oxide layers less than 3–4 nm thick
  direct tunneling through the silicon oxide layer
  Mechanisms
    Electron tunneling in the conduction band (ECB)
    Electron tunneling in the valence band (EVB)
    Hole tunneling in the valence band (HVB)

## Slide 243: Components of Gate Oxide Tunneling

## Slide 244: Fowler Nordheim Tunneling
float
0v
Igb
float
bulk
12v
FN Tunneling
Gate-Bulk
0v
12v
5v
-12v
Igs
float
FN Tunneling
Gate-Source

## Slide 245: Electron Tunneling
Vtun
Increasing the applied voltage decreases the effective barrier width
The range of tunneling currents span many orders of magnitude.

## Slide 246: What governs tunneling rate?
Oxide Thickness
Field applied across the oxide.
  Vtun ~ 30v for 2.0um
  Vtun ~ 20v for 1.2um
  Vtun ~ 15v for .5um
  Vtun ~ 12v for .3um
FLASH

## Slide 248: EEPROMS
EEPROMS allow transport of electrons to and from gate
Oxide between floating gate and channel in thinned out partially
  To enhance tunneling
  FLOTOX process
    Floating Gate Tunneling Oxide
  Poly2 makes control gate and wordline poly

## Slide 249: FLOTOX EEPROM
Floating gate
Source
Substrate
p
Gate
Drain
n
1
n
1
FLOTOX transistor
Fowler-Nordheim I-V characteristic
20
–
30 nm
10 nm
-10 V
10 V
I
V
GD

## Slide 250: Double Poly EEPROM cell

## Slide 251: FLOTOX EEPROM Array
Program
  FNT
  Bytewise / wordwise
  Byte Select = Vpp
  W/L = Vpp
  B/Ls = 0v
Vpp
Vpp-Vt
0v
0v
FNT
Vpp-Vt
0v
Vpp
0v
FNT
Erase
  FN Tunneling
  Bytewise / wordwise / Pagewise
  Byte Select = 0v
  W/L = Vpp
  B/Ls = Vpp
Vdd/2
Vdd
Read – BL=Vdd/2 , WL = Vdd, Byte Sel = Vdd
Write = Erase then Program

## Slide 252: Flash EEPROM
Control gate
erasure
p-
substrate
Floating gate
Thin tunneling oxide
n
1
source
n
1
drain
programming
Many other options …

## Slide 255: Cross-sections of NVM cells
EPROM
Flash
Courtesy Intel

## Slide 267
8Mb core

## Slide 268: FLOTOX EEPROM Array
Program
  FNT
  Bytewise / wordwise
  Byte Select = Vpp
  W/L = Vpp
  B/Ls = 0v
Vpp
Vpp-Vt
0v
0v
FNT
Vpp-Vt
0v
Vpp
0v
FNT
Erase
  FN Tunneling
  Bytewise / wordwise / Pagewise
  Byte Select = 0v
  W/L = Vpp
  B/Ls = Vpp
Vdd/2
Vdd
Read – BL=Vdd/2 , WL = Vdd, Byte Sel = Vdd
Write = Erase then Program

## Slide 269: Flash EEPROM
Control gate
erasure
p-
substrate
Floating gate
Thin tunneling oxide
n
1
source
n
1
drain
programming
Many other options …

## Slide 272: Cross-sections of NVM cells
EPROM
Flash
Courtesy Intel

## Slide 284
8Mb core

## Slide 285
NAND
String
WL is active low, erased cell Xtor is always on, programmed cell Xtor is off
Erased = 0, Programmed = 1

## Slide 286: NOR- and NAND-type Flash cell comparison

## Slide 288
16 cells
Bitline

## Slide 291: Program Inhibit Schemes (Basic)
0v
8v
VPGM=18v
VPass=10v
VPass=10v
VPass=10v
0V
0V
Programmed cell
FN Tunneling enabled
Unprogrammed cell
FN Tunneling inhibited

## Slide 294
SA

## Slide 296: NAND Flash Pinout
No ADDR / DATA pins??

## Slide 297: NAND Flash Connectivity to System
CPU
ADDR, Data,
Command

## Slide 299: NAND Flash Page Read
Command
Phase
Address
Phase
Data Xfer
Phase
(Long ~25us)
Readout
Phase
One data / pulse

## Slide 300: NAND Flash Page Program
Command
Phase
Address
Phase
Data I/P
Phase
One data / pulse
Program
Phase
Long ~ 250uS
Check
Timeout

## Slide 301: Array Organization – Logical View
Cell -> Byte / Word -> Page -> Block
Entire Page Programmed / Read at one time
ECC

## Slide 302: Advantages of Page / Block Organisation
Eg : Page = 2KB, Block = 128Kb
The effective read speed of the large page NAND devices is similar to the small block devices:
  Read Time = 6 cycles x 50ns(command) + 25 µs(data xfer) + 2112 cycles x 50ns(readout) = 131 µs
  Read Speed = 2112 bytes / 131 µs = 16.1 Mbytes /sec
The effective write speed of the large page NAND devices is more than 3 times faster.
  Write Time = 5 cycles x 50ns + 2112 cycles x 50ns + 1 cycle x 50ns + 200µs = 306 µs
  Write Speed = 2112 bytes / 306µs = 6.9 Mbytes / sec
The effective erase speed is nearly 8 times faster.
  Erase Time = 4 cycles x 50ns + 2ms = 2ms
  Erase Speed = 128kB / 2ms = 64 Mbytes / sec

## Slide 303: 128Mb NAND Flash Functional Block Diagram

## Slide 304
All cells
on one WL
form a page
Programmed
Together
2112x8 cells
Per phys page
32
Block
32 pages
512Kbits
Write data
½ Phys page
Read data
½ Phys page
LH ½ phys page + RH ½ phys page =
1 logical page
8k+256
bits
8k+256
bits

## Slide 305
BL Direction
BL Direction
WL Direction
WL Direction
Global WL Decs
Block
SA

## Slide 306: 125mm2 1Gbit NAND Flash Memory
Technology 0.13µm p-sub CMOS triple-well
1poly, 1polycide, 1W, 2Al
Cell size 0.077µm2
Chip size 125.2mm2
Organization 2112 x 8b x 64 pages x 1k blocks
  Page = 16Kb (2KB) data 512b ECC, 1 ECC bit / 32 data bits
Power supply 2.7V-3.6V
Cycle time 50ns
Read time 25µs
Program time 200µs / page
Erase time 2ms / block

## Slide 312: Features of NAND- and NOR-type FLASH